## Slide 1: Homework 2 – Board Investigation and Discovery
STM32F429IDISCOVERY Board vs Maker Pi RP2040 - Motor and Robot Controller

## Slide 2: Hardware Diagram - STM32F429IDISCOVERY Board

## Slide 3: Board Layout - Maker Pi RP2040 - Motor and Robot Controller

## Slide 4: How much does each board cost? Are they available?
STM32F429IDISCOVERY Board
Digikey PN: 497-16140-ND
Cost: $29.00
Num in stock: 10
Maker Pi RP2040 - Motor and Robot Controller
Adafruit PN: 5129
Cost: $12.50
Num in stock: 0

## Slide 5: What kind of processor is it?
STM32F429ZIT6
ARM Cortex-M4
180MHz
Single Core
RISC
32 bit
256K SRAM
2 Mbytes Flash
https://www.st.com/en/microcontrollers-microprocessors/stm32f429zi.html
RP2040
ARM Cortex-M0+
133 MHz
Dual Core
RISC
32 bit
264K SRAM
0 Mbytes Flash
https://www.raspberrypi.com/documentation/microcontrollers/rp2040.html

## Slide 6: How much Flash and RAM does it have? Any other memory types?
STM32F429IDISCOVERY Board
64 Mbit SDRAM
2 Mbytes
Supports 64MB external memory
Maker Pi RP2040 - Motor and Robot Controller
0 SDRAM
2Mbytes Flash
Supports 16 MB external memory

## Slide 7: Does it have any special peripherals? List 3-5 that you find interesting.
STM32F429IDISCOVERY Board
Has an ST MEMS motion sensor 3-axis digital output gyroscope
2.4” QVGA TFT LCD
“Extension header for LQFP144 I/Os for a quick connection to the prototyping board and an easy probing”
This is a board optimized for debugging
Maker Pi RP2040 - Motor and Robot Controller
It has 4 Servo motors
It also has 2 DC motors with quick test buttons
There are 13 status LEDs for GPIO pins
Piezo buzzer with mute switch
7 grove ports (flexible I/O)
This is the Las Vegas of boards

## Slide 8: If it has an ADC, what are the features?
STM32F429IDISCOVERY Board
3×12-bit, 2.4 MSPS ADC: up to 24 channels and 7.2 MSPS in triple interleaved mode
Maker Pi RP2040 - Motor and Robot Controller
N/A

## Slide 9: Look at one application note for this board
STM32F429IDISCOVERY Board
Looked at: EMC design guide for STM8, STM32 and Legacy MCUs
https://www.st.com/resource/en/application_note/an1709-emc-design-guide-for-stm8-stm32-and-legacy-mcus-stmicroelectronics.pdf
Maker Pi RP2040 - Motor and Robot Controller
So far unable to find application notes for this board

## Slide 10: Sources:
STM32F429IDISCOVERY Board
  https://www.st.com/content/ccc/resource/technical/document/data_brief/ff/c1/b6/02/c3/b4/49/cb/DM00094498.pdf/files/DM00094498.pdf/jcr:content/translations/en.DM00094498.pdf
  https://www.st.com/en/microcontrollers-microprocessors/stm32f429ii.html#documentation
  https://www.st.com/en/microcontrollers-microprocessors/stm32f429ii.html#
  https://www.st.com/en/microcontrollers-microprocessors/stm32f429zi.html
Maker Pi RP2040 - Motor and Robot Controller
  https://www.adafruit.com/product/5129
  https://www.raspberrypi.com/documentation/microcontrollers/rp2040.html
  https://docs.google.com/document/d/1DJASwxgbattM37V4AIlJVR4pxukq0up25LppA8-z_AY/edit
  https://www.cytron.io/p-maker-pi-rp2040-simplifying-robotics-with-raspberry-pi-rp2040